## Slide 1: CS161 – Design and Architecture of Computer Systems
Week 1 - Discussion
*some slides adapted from:
Prof Daniel Wong UCR – EE/CS)

## Slide 2: Welcome!

## Slide 3: About TA
Jason Zellmer
UC Riverside, CA
  PhD Computer Science ’18--present
  MSc Statistics ’18
University of Wisconsin-Milwaukee, WI
  BSc Mathematics ’15
Research area: Architecture Security
Email: jzell001@ucr.edu
Office Hours: TBD or by appointment

## Slide 4: Discussion Format
Purpose:
  Supplement lecture material
  Answer questions
What we’ll be doing:
  Practice problems
  Reviewing homework/etc.
  Preparing for exams

## Slide 5: CPU Clocking
Clock (cycles)
Clock period
Clock period: duration of a clock cycle (0.25ns)
Clock rate: cycles per second (4.0GHz)

## Slide 6: CPU Clocking
Clock period: seconds per cycle
  1 cs (centisecond)
  1 ms (millisecond)
  1 s (microsecond)
  1 ns (nanosecond)
  1 ps (picosecond)
Clock rate: cycles per second (Hertz = frequency)
  1 KHz (Kilohertz)
  1 MHz (Megahertz)
  1 GHz (Gigahertz)

## Slide 7: CPU Clocking
Example 1:
Clock Rate = 1 GHz =
Clock Period =
Example 2:
Clock Rate = 4 GHz =
Clock Period =

## Slide 8: Instruction Count and CPI
Instruction Count (IC)
  number of instructions for a program
  (instructions: ADD, LOAD, etc.)
Cycles Per Instruction (CPI)
  average number of clock cycles per instruction for a program

## Slide 9: CPI (more detail)
For different instruction types:
Weighted average CPI:

## Slide 10: CPI Example
Alternative compiled code sequences using instructions in type INT, FP, MEM
Program 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Program 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5
Type | INT | FP | MEM
CPI for type | 1 | 2 | 3
IC in Program 1 | 2 | 1 | 2
IC in Program 2 | 4 | 1 | 1

## Slide 11: Amdahl’s Law
Improving one aspect of performance does not always have a proportional affect on overall performance

## Slide 12: Amdahl’s Law: Example
Enhancement 1:
Speedup of 20 on 10% of execution time
Enhancement 2:
Speedup of 1.6 on 80% of execution time
When we are about to speed up only a part of the program
What is the overall speedup on the entire program?
Example: We have two possible enhancements, what is the overall
speedup on the entire program for each one?
1.105
1.43

## Slide 13: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second

## Slide 14: Practice Problems
Processor 1 runs at 1GHz with a CPI = 1, Processor 2 runs at 4GHz with a CPI=7. Calculate the Million of Instructions per Second (MIPS). Which one runs faster?
Calculate the Average CPI of the two programs
Profiling a program, you see that a single function takes 15% of the total execution time. Through various optimizations, you’ve speed up this function a 3x. What is the speedup of the entire application?
 | INT | FP | MEM | BEQ
CPI | 2 | 4 | 5 | 1
P1 | 2 | 1 | 2 | 2
P2 | 4 | 2 | 1 | 3