## Slide 1: CS161 – Design and Architecture of Computer Systems
Week 2 - Discussion
*some slides adapted from:
Prof Daniel Wong UCR – EE/CS)

## Slide 2: MIPS Registers
32 × 32-bit registers (0-31)
Assembly register names
Register File
0
32 bits
R0
32 Registers
R1
R2
…
1 word

## Slide 3: Memory
4 Billion Memory Locations
8 bits (byte)
Memory
0
1
2
…
4,294,967,295
(=232 -1)
1 word
4-byte aligned:
  each location is one byte
  4 bytes (32 bits) = word
  4 locations per instruction
3

## Slide 4: Memory and Register File
R31
32 Registers
4 Billion Memory Locations
32 bits (4 bytes)
8 bits (byte)
0
Memory
Register File
0
1
2
4,294,967,295
(=232 -1)
R0
R1
R2
1 word
1 word
  only load/store access memory
  32-bit data called a “word”
  4 bytes/instruction
  4-byte aligned
3
…
…

## Slide 5: Memory Operand Example
C code:
  $s2 = h, $s3 = base address of array A
  A[12] = h + A[8];
MIPS code:
  index 8  offset of 32
  index 12  offset of 48
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 6: MIPS Assembly Instructions

## Slide 7: MIPS Instruction Format
  op: operation code
  rs: src register
  rt: src register (R-type) / dst register (I-type)
  rd: dst register
  shamt: shift amount (shift left logical – sll amount)
  funct: function code (extends opcode)
Notes: Quickly.

## Slide 8: R-format Example: add
add $r8, $r17, $r18 (add rd, rs, rt)
special
$r17
$r18
$r8
0
add
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 9: R-format Example: sll
special
$r17
0
$r8
2
sll
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
shamt: shift amount (# positions to shift)
Shift Left Logical (sll)
  sll by i bits multiplies by 2 x i
  i.e., above 2 x 2 =4
sll $r8, $r17, 2 (sll rd, rs, shamt)

## Slide 10: sll Example
C code:
  $s0 = i, $s1 = j, $s2 = base address of array A
  j = A[i];
MIPS code:
  index i  offset of i x 4
sll $t0, $s0, 2 # $t0 = i x 4 add $t0, $t0, $s2 # $t0 = &A[i] lw $s1, 0($t0) # $s1 = A[i]

## Slide 11: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to + (215 – 1), used as immediate
  Address: offset added to base address in rs
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits

## Slide 12: I-format Example: load
lw $r8, 8($r17), $r8  Mem[8+$r17]
lw
$r17
$r8
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits
8
  rs: src register
  rt: dst register

## Slide 13: I-format Example: store
sw $r8, 8($r17), Mem[8+$r17]  $r8
sw
$r17
$r8
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits
8
  rs: src register
  rt: src register

## Slide 14: I-format Example: addi
addi $r8,$r17, 8 $r8  8+$r17
addi
$r17
$r8
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits
8

## Slide 15: I-format Example: beq
beq $r8,$r17, 8 if ($r8==$r17) PC  PC+4 + 8x4
beq
$r17
$r8
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
8
Most branch targets near branch
PC-relative addressing
  Target address = PC + offset x 4
  (PC already incremented by 4 by this time)

## Slide 16: If Statements (branches)
C code:
  $s0 = f, $s1 = g, $s2 = h, $s3 = i, $s4 = j
  if (i==j)
  f = g+h; else
  f = g-h;
MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …

## Slide 17: More Conditional Operations
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L
  L

## Slide 18: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$zero
1111 1111 1111 1111 1100 0011 1111 1111
$t1
Register 0: always read as zero
0000 0000 0000 0000 0000 0000 0000 0000
$t0
Notes: nor $s1, $s2, $s3 $s1 = ~ ($s2 | $s3) Three reg. operands; bit-by-bit NOR
So if you make $s3 all zeros, then it is the traditional NOT instruction for (NOT $s2)

## Slide 19: Amdahl’s Law
One improvement at a time:
Multiple improvements at once:

## Slide 20: Instructions Per Cycle (IPC)
Cycles Per Instruction (CPI)
Instructions Per Cycle (IPC)
Relationship:

## Slide 21: Practice Problems
Convert the following C code to MIPS assembly. Assume ‘i’ is held in $s0 and ‘j’ is held in $s1
if (i > j) {
j++;
}
else if (i == j ) {
i++;
}
else {
i = j+i
}
2) Convert the following MIPS assembly
to C code, where $s0, $s1, and $s2 are
variables i, j, and k, respectively and
$s3 is a pointer to an array A (i.e., the
base address of array A)
sll $t0, $s0, 2
add $t0, $t0, $s3
lw $s1, 0($t0)
addi $s0, $s0, 1
sll $t0, $s0, 2
add $t0, $t0, $s3
lw $s2, 0($t0)
add $t0, $s1, $s2
sw $t0, 12($s3)

## Slide 22: CS161 – Design and Architecture of Computer Systems
CHP 3

## Slide 23: Datapath

## Slide 24: Datapath
Register File
I-Memory/Cache
D-Memory/Cache

## Slide 25: Instruction Flow
  IF - Instruction fetch
  ID - Instruction decode and register operand fetch
  EX - Execute/Evaluate memory address
  MEM - Memory operand fetch
  WB - Store/writeback result
IF
ID
EX
WB
MEM

## Slide 26: R-type Instructions – ADD Instruction
0
6-bit
rs
5-bit
rt
5-bit
rd
5-bit
0
5-bit
ADD
6-bit
ADD rd, rs, rt
if MEM[PC] == ADD rd rs rt
GPR[rd]  GPR[rs] + GPR[rt]
PC  PC + 4
ALU-Type
(ADD R3, R2, R1)
IF
ID/RF
EX
WB to Reg.
rs
rt
rd

## Slide 27: I-type Instructions - ADDI Instruction
ADDI
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
ADDI rt, rs, immediate
if MEM[PC] == ADDI rt rs immediate
GPR[rt]  GPR[rs] + sign-extend (imm)
PC  PC + 4
rs
rt
rd
ALU-Type
(ADD R3, R2, R1)
IF
ID/RF
EX
WB to Reg.

## Slide 28: I-type Instructions - LW Instruction
LW
6-bit
rs
5-bit
rt
5-bit
offset
16-bit
LW rt, offset(rs)
if MEM[PC]==LW rt offset16 (base)
Addr = sign-extend(offset) + GPR[base]
GPR[rt]  MEM[Addr]
PC  PC + 4
LW
(LW R2, 4(R1))
IF
ID/RF
EX
MEM
WB to Reg.
rs
rt
rd

## Slide 29: I-type Instructions - SW Instruction
SW
6-bit
rs
5-bit
rt
5-bit
offset
16-bit
SW rt, offset(rs)
if MEM[PC]==SW rt offset16 (base)
Addr = sign-extend(offset) + GPR[base]
MEM[Addr]  GPR[rt]
PC  PC + 4
SW
(SW R2, 8(R1))
IF
ID/RF
EX
MEM
rs
rt
rd

## Slide 30: I-type Instructions - Branch Instructions
BEQ
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
BEQ rs, rt, immediate
if MEM[PC]==BEQ rs rt immediate16
target = PC + 4 + sign-extend(immediate) x 4
if (GPR[rs]==GPR[rt]) PC  target
else PC  PC + 4
rs
rt
rd
BEQ
(BEQ R3, R1, displace)
IF
ID/RF
EX(compare)
Potentially Update PC = PC+disp

## Slide 31: J-type Instructions - Jump Instructions
J
6-bit
immediate
26-bit
J immediate
if MEM[PC]==J immediate26
target = { PC[31:28], immediate26, 2’b00 }
PC  target
J
(J displace)
IF
ID/RF
Update PC = PC+disp+00

## Slide 32: Single Cycle Implementation
Calculate cycle time assuming negligible delays except:
  memory (2ns), ALU and adders (2ns), register file access (1ns)

## Slide 33: Instruction Flow
Calculate cycle time assuming negligible delays except:
  memory (2ns), ALU and adders (2ns), register file access (1ns)
IF
ID
EX
WB
MEM

## Slide 34: Single Cycle – How long is the cycle?
Inst. Type | Inst. Mem. | Reg. File (read) | ALU (s) | Data Mem. | Reg. File (write) | Total
R-type | 2 | 1 | 2 | 0 | 1 | 6 ns
Load | 2 | 1 | 2 | 2 | 1 | 8 ns
Store | 2 | 1 | 2 | 2 | 0 | 7 ns
Branch | 2 | 1 | 2 | 0 | 0 | 5 ns
Jump | 2 | 0 | 0 | 0 | 0 | 2 ns
The cycle time must accommodate the longest operation: lw.
Cycle time = 8 ns but the CPI = 1.
If we can accommodate variable number of cycles for each instruction and a cycle time of 1ns.
CPI = 6*44% + 8*24% + 7*12% + 5*18% + 2*2% = 6.3
Inst. %
44
24
12
18
2

## Slide 35: Control Signals