## Slide 1: CS161 – Design and Architecture of Computer Systems
Week 3 – Discussion
*some slides adapted from:
Prof Daniel Wong UCR – EE/CS)

## Slide 2: Multicycle
Divides operations into steps
One cycle per step
Critical Path: longest functional unit per step (i.e., PC+4 vs I-Mem)
IF
ID
EX
WB
MEM

## Slide 3: Multicycle
0
Instruction
Fetch
1
Instruction
Decode
2
Mem. Address
Compute
3
Mem. Access
Read
5
Mem. Access
Write
4
Write-Back
6
ALU
Execute
7
Complete
R-type
8
Complete
Branch
9
Complete
Jump
Start
Op = LW or SW
Op = R-type
Op = BEQ
Op = J
Op = SW
Op = LW
Load = 5 cycles (IF, ID, EX, MEM, WB)
Store = 4 cycles (IF, ID, EX, MEM)
R-type = 4 cycles (IF, ID, EX, WB)
Branch = 3 cycles (IF, ID, EX)
Jump = 3 cycles (IF, ID, Jump)

## Slide 4: Control Signals
Notes: Quickly.

## Slide 5: Multicycle
Load = 5 cycles (IF, ID, EX, MEM, WB)
Store = 4 cycles (IF, ID, EX, MEM)
R-type = 4 cycles (IF, ID, EX, WB)
Branch = 3 cycles (IF, ID, EX)
Jump = 3 cycles (IF, ID, Jump)

## Slide 6: ALU Control Signals
ALU Control input
  function field of the instruction
  2-bit control field (ALUOp)
ALUOp indicates operation
  (00) add - for loads and stores
  (01) subtract - for beq
  (10) determined by funct field
ALU Control output:
  4-bit ALU control signal lines
  Note: Operation3 used only for NOR function
Notes: A confusing aspect of Figure D.2.2 is that there is no logic function for Operation3.
That is because this control line is only used for the NOR operation, which
is not needed for the MIPS subset in Figure 4.12

## Slide 7: Control Signal Example: SWAP

## Slide 8: Control Signal Example: SWAP
Add any necessary changes to datapath

## Slide 9: Control Signal Example: SWAP

## Slide 10: Control Signal Example: SWAP
Add any necessary changes to control signals

## Slide 11: Control Signal Example: SWAP

## Slide 12: Multicycle  Pipeline
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
We can overlap instructions

## Slide 13: Problem: Account for Delays
$s0 data not ready
Need to stall

## Slide 14: Solution: Forwarding
  Forward data as soon as it’s available
Forwarding

## Slide 15: When to Forward
= Forwarding

## Slide 16: When to Forward
1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
If dest == either src register
Fwd from EX/MEM pipeline reg
If dest == src register
Fwd from MEM/WB pipeline reg
But only if forwarding instruction will write to register
  EX/MEM.RegWrite
  MEM/WB.RegWrite
rs
rt
rd

## Slide 17: With Forwarding
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
    ForwardA = 10 (where b10 = #2)
rs
rt
rd

## Slide 18: With Forwarding
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
    ForwardB = 10 (where b10 = #2)
rs
rt
rd

## Slide 19: With Forwarding
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
    ForwardA = 01 (where b01 = #1)
rs
rt
rd

## Slide 20: With Forwarding
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
    ForwardB = 01 (where b01 = #1)
rs
rt
rd

## Slide 21: Still Can’t Avoid All Stalls
Can’t “forward” data backwards
Still need to stall for one cycle

## Slide 22: Solution: LW Stalls
Instruction reordering to fill stalls
Stall
Stall

## Slide 23: LW Forwarding Example 1
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t3, 12($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t4, 8($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t5, 16($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
With no forwarding enabled

## Slide 24: LW Forwarding Example 1
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  | F | - | - | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Wait on $t2, stall 2 cycles
sw $t3, 12($t0) |  |  |  |  |  | F | - | - | D | E | M | W |  |  |  |  |  |  |  | Wait on $t3, stall 2 cycles
lw $t4, 8($t0) |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  | F | - | - | D | E | M | W |  |  |  | Wait on $t4, stall 2 cycles
sw $t5, 16($t0) |  |  |  |  |  |  |  |  |  |  |  |  | F | - | - | D | E | M | W | Wait on $t5, stall 2 cycles
With no forwarding enabled (dependencies)

## Slide 25: LW Forwarding Example 2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t3, 12($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t4, 8($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t5, 16($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
With forwarding enabled

## Slide 26: LW Forwarding Example 2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  | F | - | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  | Forward $t2 from Mem/WB to Exec, Stall 1 cycle
sw $t3, 12($t0) |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Forward $t3 from Exec/Mem to Exec.
lw $t4, 8($t0) |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  | F | - | D | E | M | W |  |  |  |  |  |  |  | Forward $t4 from Mem/WB to Exec, Stall 1 cycle
sw $t5, 16($t0) |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  | Forward $t5 from Exec/Mem to Exec.
With forwarding enabled (dependencies – forwarding)

## Slide 27: LW Forwarding Example 3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t3, 12($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t4, 8($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t5, 16($t0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
With forwarding and reordering enabled

## Slide 28: LW Forwarding Example 3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t4, 8($t0) |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  | Forward $t2 from Mem/WB to Exec.
sw $t3, 12($t0) |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Forward $t3 from Exec/Mem to Exec.
add $t5, $t1, $t4 |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
sw $t5, 16($t0) |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | Forward $t5 from Exec/Mem to Exec.
With forwarding and reordering enabled (dependencies – forwarding)

## Slide 29: Problem: Branch Hazard
If branch determined in MEM
Flush these instructions

## Slide 30: Solution: Branch Hazard
Move hardware determine outcome in ID stage
  Target address adder
  Register comparator
Use branch prediction (history of branches) & instruction reordering

## Slide 31: Branch Forwarding Example 1
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t1, $t3, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Branch Taken case
Branches resolve in MEM, with forwarding enabled. Assume stall on branch (i.e., no branch predictor)

## Slide 32: Branch Forwarding Example 1
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | - | - |  |  |  |  |  |  |  |  | (Stall 2 cycles on branch)
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  | F | D | E | M | W |  |  |  | Fetch target in cycle 6 because branch is now resolved
Branches resolve in MEM, with forwarding enabled. Assume stall on branch (i.e., no branch predictor)
Branch Taken case

## Slide 33: Branch Forwarding Example 2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t1, $t3, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Branches resolve in MEM with forwarding enabled. Assume no stall on branch, so next instruction can be fetched right after branch (i.e., branch predictor). Assume always not-taken predictor.
Branch Taken case

## Slide 34: Branch Forwarding Example 2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | F | D |  |  |  |  |  |  |  |  | Branch predicted as not-taken
add $t5, $t1, $t4 |  |  |  |  | F |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  | F | D | E | M | W |  |  |  | Fetch target in cycle 6 because branch is now resolved
Branch Taken case
Branches resolve in MEM with forwarding enabled. Assume no stall on branch, so next instruction can be fetched right after branch (i.e., branch predictor). Assume always not-taken predictor.

## Slide 35: Branch Forwarding Example 3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t1, $t3, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Branches resolve in MEM, with forwarding enabled. Assume stall on branch (i.e., no branch predictor)
Branch Not Taken case

## Slide 36: Branch Forwarding Example 3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  | - | - | F | D | E | M | W |  |  |  | Branch resolves in cycle 6 (Stall 2 cycles on branch)
add $t5, $t1, $t4 |  |  |  |  |  |  | F | D | E | M | W |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  | F | D | E | M | W |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  |  |  | F | D | E | M | W | 
Branch Not Taken case
Branches resolve in MEM, with forwarding enabled. Assume stall on branch (i.e., no branch predictor)

## Slide 37: Branch Forwarding Example 4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t1, $t3, $t2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
tgt: lw $t1, 8($t2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Branches resolve in MEM, with forwarding enabled. Assume no stall on branch, so next instruction can be fetched right after branch (i.e., branch predictor). Assume always taken predictor.
Branch Not Taken case

## Slide 38: Branch Forwarding Example 4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Comments
lw $t1, 8($t2) | F | D | E | M | W |  |  |  |  |  |  |  |  | 
add $t4, $t5, $t6 |  | F | D | E | M | W |  |  |  |  |  |  |  | 
beq $t1, $t4, tgt |  |  | F | D | E | M | W |  |  |  |  |  |  | Cycle 5, forward $t1 and $t4
add $t1, $t3, $t2 |  |  |  |  |  | F | D | E | M | W |  |  |  | Branch resolved in cycle 6. Misprediction!
add $t5, $t1, $t4 |  |  |  |  |  |  | F | D | E | M | W |  |  | 
add $t3, $t2, $t4 |  |  |  |  |  |  |  | F | D | E | M | W |  | 
tgt: lw $t1, 8($t2) |  |  |  | F | D |  |  |  |  |  |  |  |  | (assumes branch taken)
Branch Not Taken case
Branches resolve in MEM, with forwarding enabled. Assume no stall on branch, so next instruction can be fetched right after branch (i.e., branch predictor). Assume always taken predictor.

## Slide 39: Practice Midterm

## Slide 40: Practice Midterm
Notes: Since the largest instruction type (Load) takes 8 ns, then the clock cycle time for a single cycle must be 8 ns.
For a single cycle, there is only one cycle for each instruction, and since CPI = cycles/instruction, then CPI = 1 for single cycle

## Slide 41: Practice Midterm

## Slide 42: Practice Midterm
R-type = 4 cycles (IF, ID, EX, WB)  4*.4
Load = 5 cycles (IF, ID, EX, MEM, WB)  5*.2
Store = 4 cycles (IF, ID, EX, MEM)  4*.1
Branch = 3 cycles (IF, ID, EX)  3*.2
Jump = 3 cycles (IF, ID, Jump)  3*.1
Notes: R-type need 4 cycles (IF, ID, EX, WB)  4*.4
Load has 5 cycles (IF, ID, EX, MEM, WB)  5*.2
Store need 4 cycles (IF, ID, EX, MEM)  4*.1
Branch has 3 cycles (IF, ID, EX)  3*.2
Jump has 3 cycles (IF, ID, Jump)  3*.1

## Slide 43: Practice Midterm

## Slide 44: Practice Midterm
Notes: CPU Time = clock cycles * (CPI * Instruction Count) = (CPI * Instruction Count) / clock rate
clock cycle = 1/(clock rate) = 1/(500 MHz) = 1/(500*10^6) = 1/(0.5*10^9) = 2*10^(-9) = 2 ns

## Slide 45: Practice Midterm

## Slide 46: Practice Midterm

## Slide 47: Practice Midterm

## Slide 48: Practice Midterm

## Slide 49: Practice Midterm

## Slide 50: Practice Midterm

## Slide 51: Practice Midterm

## Slide 52: Practice Midterm

## Slide 53: Practice Midterm

## Slide 54: Practice Midterm

## Slide 55: Practice Midterm

## Slide 56: Practice Midterm
0
1
2

## Slide 57: Practice Midterm

## Slide 58: Practice Midterm