## Slide 1: CS161 – Design and Architecture of Computer Systems
Week 4 - Discussion

## Slide 2: Midterm Review
1. (8 points) Compute the CPI for this program on this CPU.
CPI = 0.44*2 + 0.24*4 + 0.12*1 + 0.16*4 + 0.04*4
= 0.88 + 0.96 + 0.12 + 0.64 + 0.16
= 2.76 cycles/instruction
2. (8 points) A new compiler reduces the number of Conditional Branches by half, compute
the new CPI.
new CPI = (0.44*2 + 0.24*4 + 0.12*1 + 0.08*4 + 0.04*4) / 0.92
= (0.88 + 0.96 + 0.12 + 0.32 + 0.16 ) / 0.92
= 2.65 cycles/instruction (regrade?)

## Slide 3: Midterm Review
3. (2 points each) Name the three types of pipeline hazards and name three
solutions discussed in class.
Hazards: Solutions 1. Structural Hazard 1. Stall 2. Data Hazard 2. Forwarding 3. Control Hazard 3. Reorder Instructions 4. (8 points) Write the MIPS code corresponding to this C code. Assume i and k correspond to
$s3 and $s5 while the base of the array is at $s6.
While (save[i] == k)
i += 1;
LOOP : sll $t0, $s3, 2 # $t0 = i * 4
add $t0, $t0, $s6 # $t0 = &save[i]
lw $t1, 0($t0) # $t1 = save[i]
bne $t1, $s5, EXIT # if (save[i] != k) goto EXIT
addi $s3, $s3, 1 # i = i + 1
j LOOP # goto LOOP
EXIT:

## Slide 4: Midterm Review
5. (8 points) Given the MIPS instruction lw $t0, 4($s0) explain how the 32 bits of the instruction
word will be allocated.
lw rt, imm(rs) # rt ← Mem[imm+rs]
lw $t0, 4($s0) # $r0 ← Mem[4+$s0]
[31-26]: opcode (lw)
[25-21]: register source ($s0)
[20-16]: register destination ($t0)
[15-0]: immediate(#4)

## Slide 5: Midterm Review
rs
rt
rd
x
x
x
x
6. (8 points) Given the MIPS instruction sw R0, 8(R0), determine the necessary control signals.

## Slide 6: Midterm Review
rs
rt
rd
7. (8 points) Trace the datapath that is active during the sw R0, 8(R0) instructi

## Slide 7: Midterm Review
8. (8 points) Separate the following datapath into stages of the pipeline discussed in class. Label each stage clearly.
IF
ID
EX
WB
MEM

## Slide 8: Midterm Review
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  | F | - | - | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Wait on $t2, stall 2 cycles
sw $t3, 12($t0) |  |  |  |  |  | F | - | - | D | E | M | W |  |  |  |  |  |  |  | Wait on $t3, stall 2 cycles
lw $t4, 8($t0) |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  |  |  |  | F | - | - | D | E | M | W |  |  |  | Wait on $t4, stall 2 cycles
sw $t5, 16($t0) |  |  |  |  |  |  |  |  |  |  |  |  | F | - | - | D | E | M | W | Wait on $t5, stall 2 cycles
With no forwarding enabled (dependencies)
9. (8 points) Map the pipeline schedule for the code below. Assume there is no forwarding
enabled.

## Slide 9: Midterm Review
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | Comments
lw $t1, 0($t0) | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t2, 4($t0) |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t3, $t1, $t2 |  |  | F | - | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  | Forward $t2 from Mem/WB to Exec, Stall 1 cycle
sw $t3, 12($t0) |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | Forward $t3 from Exec/Mem to Exec.
lw $t4, 8($t0) |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
add $t5, $t1, $t4 |  |  |  |  |  |  | F | - | D | E | M | W |  |  |  |  |  |  |  | Forward $t4 from Mem/WB to Exec, Stall 1 cycle
sw $t5, 16($t0) |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  | Forward $t5 from Exec/Mem to Exec.
With forwarding enabled (dependencies – forwarding)
10. (8 points) Map the pipeline schedule for the code below using forwarding when necessary.

## Slide 10: CS161 – Design and Architecture of Computer Systems
Chp 5 – Memory
*some slides adapted from:
Prof Daniel Wong UCR – EE/CS)

## Slide 11: DRAM vs SRAM
Dynamic Random Access Memory (DRAM)
  slowly discharges, need to refresh to preserve
  slower  cheaper  larger (can afford more)
Static Random Access Memory (SRAM)
  no need to refresh (more transistors to “store”)
  much faster than DRAM
  faster  expensive  smaller (use less of them)
Storage | Speed | Cost | Capacity | Delay | Cost/GB
Static RAM | Fastest | Expensive | Smallest | 0.5 – 2.5 ns | $1,000’s
Dynamic RAM | Slow | Cheap | Large | 50 – 70 ns | $10’s
Hard disks | Slowest | Cheapest | Largest | 5 – 20 ms | $0.1’s

## Slide 12: Latency vs Bandwidth
Latency
  time it takes to get something
  i.e., time it takes for water to get through the hose
Bandwidth
  how much you can get per second
  i.e., how much water flowing through hose / sec

## Slide 13: Memory Hierarchy
small & fast memory  close to CPU
large & slow memory  further away

## Slide 14: Cache
Cache
  small, fast, expensive memory
  between CPU and main memory
  keeps copy of most frequently used data

## Slide 15: Locality
Temporal Locality (time)
  likely to access same data repeatedly over time
  i.e., for loops
Spatial Locality (space/area)
  likely to access data close together in memory
  i.e., array element accesses / instructions

## Slide 16: Simple Cache Design
Cache
index
(decimal)
(0)
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)
(13)
(14)
(15)
Memory
Address
(decimal)
but how do we know which memory address is in the cache?
cache is smaller than memory so use hash function to map memory to the cache
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
00
01
10
11
(0)
(1)
(2)
(3)
Data

## Slide 17: Adding Tags
Need to add tags to cache to:
  distinguish between different memory locations that map to same cache block
00
01
10
11
Index
Tag
Data
00
11
01
01
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 18: Putting it Together
Concatenating:
  cache block tags
  block indices
Gives us address in main memory
00
01
10
11
Index
Tag
Data
00
11
01
01
00 + 00 = 0000
11 + 01 = 1101
01 + 10 = 0110
01 + 11 = 0111
Main memory
address in cache block

## Slide 19: Valid Bit
At start  cache is empty (no valid data)
When system is initialized, all valid bits are set to 0
When data loaded into a cache block:
  corresponding valid bit is set to 1
So cache has bits to help find data within cache and verify validity
00
01
10
11
Index
Tag
Data
00
11
01
01
00 + 00 = 0000
Invalid
???
???
Main memory
address in cache block
1
0
0
1
Valid
Bit

## Slide 20: Reading From Cache (cache hit)
Lowest k bits of the block address will index a block in the cache
  block is valid (valid bit set)
  tag matches upper (m - k) bits of m-bit address
0
1
2
3
...
...
1022
1023
Index
Tag
Data
Valid
Address (32 bits)
=
To CPU
Hit
10
22
Index
Tag
32-bit memory address and a 210-byte cache (210=1024)
  data sent to CPU

## Slide 21: Loading Block Into Cache
After data read from main memory, putting a copy of that data into the cache is straightforward.
  The lowest k bits of the block address specify a cache block
  The upper (m - k) address bits are stored in the block’s tag field
  The data from main memory is stored in the block’s data field
  The valid bit is set to 1
0
1
2
3
...
...
...
Index
Tag
Data
Valid
Address (32 bits)
10
22
Index
Tag
Data
1

## Slide 22: Cache Sets and Ways
block |  |  | 
Sets: number of
cache lines
n-ways: number of blocks per line
n-way set associative
cache line

## Slide 23: Cache Sets and Ways: Example
block |  |  | 
Sets: number of
cache lines
n-ways: number of blocks per line
n-way set associative
Example: Summer Camp!
  Students go to summer camp (each student is a memory location)
  Campers are grouped by teams and given a different color shirt (colors above)
  (each shirt color is different collection of memory locations)
  Each team is assigned to a different bathroom facility
  (each set is different team’s bathroom, each team hashed to cache-line/bathroom)
  Each bathroom has same number individual toilet stalls
  (n = # toilets/team)
team 2
team 3
team 4
team 1
n toilets/team
(0)
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)
(13)
(14)
(15)
Memory
Address
(decimal)

## Slide 24: Direct-mapped Cache
block/line
16 Sets
1-way
Direct mapped cache
- Each block maps to only one cache line
- aka “1-way set associative”
Example:
Cache size = 16 blocks
1-way
16-sets
1-way set associative

## Slide 25: Direct-mapped Cache: Example
block/line
4 Sets
1-way
(0)
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)
(13)
(14)
(15)
team 2
team 3
team 4
team 1
1 toilet/team
Example: Summer Camp!
  only one toilet per team  a lot of “conflicts”

## Slide 26: Set Associative Cache
block |  |  | 
4 Sets
4-way
Example:
Cache size = 16 blocks
4-ways
4-sets
4-way set associative

## Slide 27: Cache Sets and Ways: Example
block |  |  | 
Sets: number of
cache lines
n-ways: number of blocks per line
n-way set associative
team 2
team 3
team 4
team 1
4 toilets/team
(0)
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)
(13)
(14)
(15)
Memory
Address
(decimal)
Example: Summer Camp!
  four toilets per team  less “conflicts”

## Slide 28: Fully Associative Cache
block /line |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 Sets
16-ways
Fully Associative
- Each block can be mapped to any cache line
- aka “m-way set associative”
(where m = number of cache blocks)
Example:
Cache size = 16 blocks
16-way
1-set
16-way set associative
(fully associative)

## Slide 29: Fully Associative Cache: Example
1 Set
16-ways
16 toilets
(0)
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)
(13)
(14)
(15)
Memory
Address
(decimal)
Example: Summer Camp!
  only one bathroom, but a more toilets in the bathroom

## Slide 30: Set Associative Cache Organization

## Slide 31: Cache Addressing
block |  |  | 
s-Sets: Block mapped by address
(index)
n-Ways: Block can go anywhere in cache line
m = # blocks =
n = # ways
s = # sets =
bl = block size in bytes
Tag bits (remainder) t = a-i-b | Index bits (sets) i = log2s | Offset bits (block) b = log2bl
Address
c = cache size = s * n * b
a = # address bits
i = # index bits =
b = # block bits =
t = # tag bits = a - i - b
cache line

## Slide 32: Cache Addressing: Example 1
Ex. 64KB cache, direct mapped, 16 B block
Tag bits (remainder) t = a-i-b | Index bits (sets) i = log2s | Offset bits (block) b = log2bl
Address
16 12 4
block/line
sets
1-way
Notes: 4k sets = 2^12

## Slide 33: Cache Addressing : Example 2
Ex. 64KB cache, 2-way associative, 16 B block
Address
17 11 4
block | 
sets
2-way
cache line
Tag bits (remainder) t = a-i-b | Index bits (sets) i = log2s | Offset bits (block) b = log2bl
Notes: 4k sets = 2^12

## Slide 34: Cache Addressing : Example 3
Ex. 64KB cache, fully associative, 16 B block
Address
28 0 4
sets
fully assoc.
cache line
block |  |  | 
Tag bits (remainder) t = a-i-b | Index bits (sets) i = log2s | Offset bits (block) b = log2bl
Notes: 4k sets = 2^12

## Slide 35: Measuring Cache Performance
When do we access memory?
  Instruction Fetch (I$)
    Load
    Store
  Data (D$)

## Slide 36: Cache Performance: Example
Example:
  Given:
    I-cache miss rate = 2%
    D-cache miss rate = 4%
    Miss penalty = 100 cycles
    Base (“ideal) CPI = 2
    Load & stores are 36% of instructions
  Miss cycles (penalty) per instruction
    I-cache:
    D-cache:
  Actual CPI =
  Speedup:
    Ideal CPU is times faster
0.02 × 100 = 2
    0.36 × 0.04 × 100 = 1.44
  2 + 2 + 1.44 = 5.44
5.44/2 =2.72

## Slide 37: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 38: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 39: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block